## Slide 1: JSA Quality Assessment Tool Guidelines for Assessors
Recommended minimum of one JSA Quality Assessment per work crew per month.
While approaching job location, stop, observe work activity and look for uncontrolled hazards, PPE deficiencies, location of standby / observer, etc. If deficient, these items are likely to change soon after you are noticed by the work crew.
Address initial positive and negative observations with Supervisor.
Locate JSA at job location and verify permits are attached if needed for work scope
Score each question as shown below
  3 = Meeting Expectations
  2 = Partially meets expectations and should be improved
  1 = Does not meet expectations
Utilize the Comment section to justify score as needed (examples below)
  Scored 3 for JSA being updated to reflect changes in work scope or job condition
  Scored 2 for Supervisor conducting JSA review but not soliciting feedback
  Scored 1 for JSA not being signed
Before leaving job, discuss positive and negative JSA quality observations with Supervisor
Track JSA quality Leading Indicators by Contractor or Project to determine if corrective actions are needed.
NOTE: Contractor JSA audit tool can be used instead of this tool

## Slide 2: JSA Quality Assessment Tool
JSA QUALITY ELEMENTS | EFFECTIVENESS (1-3) | COMMENTS
1. Supervisor and all workers participated in preparation of the JSA |  | 
2. JSA is reviewed by Supervisor in worker’s native language prior to starting tasks |  | 
3. JSA is signed by all workers and Supervisor |  | 
4. JSA is readily visible and appropriately maintained at job location |  | 
5. JSA addresses immediate response to alarm (i.e., egress from confined space) |  | 
6. Task section clearly outlines the scope of work and is broken down into sufficient number of task steps |  | 
7. Hazards identified are specific (i.e., what could hurt you?, where is the hazard?, what could go wrong?) and clearly correspond to each task step |  | 
8. Mitigations for hazards are specific (quantifiable, observable) for each hazard and prevention of hazard is addressed (i.e., required PPE is listed on JSA) |  | 
9. High Consequence Potential activities have been identified and mitigations are in place |  | 
10. Field observations at job location indicate all workers are following JSA (i.e., all PPE is properly used by workers) |  | 
11. Selected worker demonstrates understanding of hazards for task on JSA |  | 
12. JSA is marked up in the field to reflect changes in the work scope, job condition, or insights from the toolbox talk |  | 
TOTAL SCORE |  | 
OVERALL % (100 x Total Score / 36) |  | 
Score | Effectiveness
3 | Meets expectations
2 | Partially meets expectations and should be improved
1 | Does not meet expectations
Assessor: ________________________
Job Location: _____________________
Date: _______________________
Supervisor: __________________
Customize for Project: replace with LSA / Diamond Event / Life Saving Rule / Life Critical Action, etc, as appropriate